## Slide 1
indoor
Small office
Large space
WBGT: wet bulb glob temperature
CAV: clothing adjustment value
RAL: recommended alert limit
outdoor
(WBGT+CAV)/RAL < 0.8
(WBGT+CAV)/RAL < 1
(WBGT+CAV)/RAL < 1.2
(WBGT+CAV)/RAL > 1.2
CAV > 0
Activity > 300W
Activity > 300W
CAV > 0
CAV > 0
Activity > 300W
Adjust clothing tips
Reschedule tips
PHS sweat > 500g/h
PHS sweat > 500g/h
Hydration tips
Activity > 300W
Activity > 300W
Activity > 300W
Fan tips
always
ClimApp is designed to support appropriate thermal behavior.
The information cannot substitute for your own personal experience and using common sense.

## Slide 2
PMV: Predicted Mean Vote
indoor
PMV < 1
PMV < 2
PMV < 3
PMV <4
CAV > 0
Activity > 300W
Activity > 300W
CAV > 0
CAV > 0
Activity > 300W
Adjust clothing tips
Reschedule tips
always
always
Hydration tips
always
ClimApp is designed to support appropriate thermal behavior.
The information cannot substitute for your own personal experience and using common sense.
always
always
Fan tips
always
Activity > 180W
Activity > 180W
Cooling vest tips
Activity > 180W

## Slide 3: Adjust clothing tips
CAV > 0
Safe reduction in clothing insulation may lower heat stress
CAV: clothing adjustment value

## Slide 4: Reschedule tips
Activity > 300W
Resting may lower heat stress

## Slide 5: Fan tips (outdoor)
Activity > 300W
Tair < 34°C
Increased airflow may be beneficial, even if skin is dry.
Tair < 43°C
Increased airflow may be beneficial if skin is wet. Externally applied water to the skin (e.g. spray; instead of only relying on sweating) will reduce the risk of dehydration, and potentially enhance the fan benefit.
20% <RH < 50%
Covering clothing = true
Tair < 43°C
Increased airflow may be beneficial if skin is wet. Externally applied water to the skin (e.g. spray; instead of only relying on sweating) will reduce the risk of dehydration, and potentially enhance the fan benefit."
40% <RH < 70%
Covering clothing = false
Tair < 43°C
RH < 40%
Covering clothing = false
Externally applied water to the skin (e.g. spray; instead of only relying on sweating) will reduce the risk of dehydration
Tair > 43°C
Increased airflow is not recommendend when air temperature exceeds 43°C.

## Slide 6: Fan tips (indoor – small office)
always
Tair < 34°C
Increased airflow may be beneficial, even if skin is dry.
Tair < 43°C
Increased airflow may be beneficial if skin is wet. Externally applied water to the skin (e.g. spray; instead of only relying on sweating) will reduce the risk of dehydration, and potentially enhance the fan benefit.
20% <RH < 50%
Covering clothing = true
Tair < 43°C
Increased airflow may be beneficial if skin is wet. Externally applied water to the skin (e.g. spray; instead of only relying on sweating) will reduce the risk of dehydration, and potentially enhance the fan benefit."
40% <RH < 70%
Covering clothing = false
Tair < 43°C
RH < 40%
Covering clothing = false
Externally applied water to the skin (e.g. spray; instead of only relying on sweating) will reduce the risk of dehydration
Tair > 43°C
Increased airflow is not recommendend when air temperature exceeds 43°C.

## Slide 7: Fan tips (indoor – large area)
always
Tair < 34°C
Increased airflow may be beneficial, even if skin is dry.
Tair < 43°C
Increased airflow may be beneficial if skin is wet. Externally applied water to the skin (e.g. spray; instead of only relying on sweating) will reduce the risk of dehydration, and potentially enhance the fan benefit.
20% <RH < 50%
Covering clothing = true
Tair < 43°C
Increased airflow may be beneficial if skin is wet. Externally applied water to the skin (e.g. spray; instead of only relying on sweating) will reduce the risk of dehydration, and potentially enhance the fan benefit."
40% <RH < 70%
Covering clothing = false
Tair < 43°C
RH < 40%
Covering clothing = false
Externally applied water to the skin (e.g. spray; instead of only relying on sweating) will reduce the risk of dehydration
Tair > 43°C
Increased airflow is not recommendend when air temperature exceeds 43°C.

## Slide 8: Cooling vest tips
always
PMV < 2
High temperature phase change material (between 21°C and 24°C) may improve your comfort and lower skin temperature but will not affect core temperature
Low temperature phase change material (between 6°C and 18°C) may be used to cool down during short breaks
(WBGTindoor+CAV)/RAL > 1
A ventilated vest may be beneficial to increase the work time ->depends highly on the environmental conditions, activity level and clothing

## Slide 9: Hydration tips
PHS sweat > 500g/h
Be aware to compensate your sweat loss.
Always